Republic of the Philippines

Department of Education

PUBLIC TECHNICAL-VOCATIONAL

HIGH SCHOOLS

Competency Based Learning Material

Module #5 Diagnosing and Troubleshooting Computer Systems

Unit of Competency: Diagnose and Troubleshoot Computer Systems

Qualification Computer Hardware Servicing II

TABLE OF CONTENTS

Page

How to Use this Module	i					                              1

Introduction	ii

Technical Terms	iii

Learning Outcome   1	1

Information Sheet 1.1	3

Operation Sheet 1.1 	6

Information Sheet 1.2	7

Self Check 1.1	10

Learning Outcome 2	11

Information Sheet 2.1	12

Information Sheet   2.2	15

Operation Sheet 2.1	17

Learning Outcome 3	18

Information Sheet 3.1	 19

Self Check 3.1	23

Information Sheet 3.2.	24

Operational Sheet 3.1	32

Learning Outcome 4	33

Information Sheet 4.1	34

Operational Sheet 4.1	39

Information Sheet 4.2	41

Operational Sheet 4.2	44

Self Check 4.1	45

Answer Keys	46

Acknowledgement

ACKNOWLEDGEMENT

Copyright Department of Education 2008

First Published JUNE 2008

This module was based on the Competency-Based Curriculum–Contextual Learning Matrix (CBC-CLM) and finalized on the Instructional Modules Finalization Development Workshop conducted at the Development Academy of the Philippines, Tagaytay City, on May 6-10, 2008.

This learning instrument was developed by the following personnel:

Technology Teachers:

Mr. Jemuel Jay E. Ybanez

Don Alejandro Roces Sr. Science Technology

Mr. Joselito H. Zapanta

General Mariano Alvarez Technical High School

Mrs. Mirasol F. Dasig

San Pedro Relocation Center National High School

Ms. Evelyn U. Escario

Don Alejandro Roces Sr. Science Technology

Ms. Cherlyn F. de Luna

Assemblywoman Felicita G. Bernardino Memorial Trade School

Contextual Teacher:

Mrs. Ma. Josefina Bueno-Luna

E. Rodriuez Vocational High School

Encoder:

Mrs. Marites L. Telewik

Milagros P. Aguihap

Deped

Nelson L. Clerigo

This work was produced with funding provided by the Department of Education.

HOW TO USE THIS MODULE

Welcome to the Module “Computer Hardware Servicing NC II”. This module contains training materials and activities for you to complete.

The unit of competency “Diagnose and Troubleshoot Computer Systems” contains knowledge, skills and attitudes required for a Computer Hardware Servicing NC II course.

You are required to go through a series of learning activities in order to complete each of the learning outcomes of the module. In each learning outcome there are Information Sheets, Job Sheets, Operation Sheets, and Activity Sheets. Follow these activities on your own and answer the Self-Check at the end of each learning activity.

If you have questions, don’t hesitate to ask your teacher for assistance.

Recognition of Prior Learning (RPL)

You may already have some of the knowledge and skills covered in this module because you have:

been working for some time

Already have completed training in this area.

If you can demonstrate to your teacher that you are competent in a particular skill or skills, talk to him/her about having them formally recognized so you don’t have to do he same training again. If you have a qualification or Certificate of Competency from previous trainings show it to your trainer. If the skills you acquired are still current and relevant to this module, they may become part of the evidence you can present for RPL. If you are not sure about the currency of your skills, discuss it with your trainer.

After completing this module ask your teacher to assess your competency. Result of your assessment will be recorded in your competency profile. All the learning activities are designed for you to complete at your own pace.

Inside this module you will find the activities for you to complete followed by relevant information sheets for each learning outcome. Each learning outcome may have more than one learning activity.

This module is prepared to help you achieve the required competency, in diagnosing and troubleshooting computer systems. This will be the source of information that will enable you to acquire the knowledge and skills independently at your own pace or with minimum supervision or help from your teacher.

Program/ Course:     Computer Hardware Servicing NC II

Unit of Competency: Diagnose and Troubleshoot Computer

System

Module:                    Diagnosing and Troubleshooting of Computer System

INTRODUCTION:

This module contains information and suggested learning activities on Computer Hardware Servicing NCII.

Completion of this module will help you better understand the succeeding module on configuring and maintaining computer systems.

This module consists of 4 learning outcomes. Each learning outcome contains learning activities supported by instruction sheets. Before you perform the instructions read the information sheets and answer the self-check and activities provided to as certain to yourself and your teacher that you have acquired the knowledge necessary to perform the skill portion of the particular learning outcome.

Upon completion of this module, report to your teacher for assessment to check your achievement of knowledge and skills requirement of this module. If you pass the assessment, you will be given a certificate of completion.

SUMMARY OF LEARNING OUTCOMES:

Upon completion of the module you should be able to:

LO1. Formulate plans and prepare for diagnostic procedure for computer    systems

LO2. Diagnose faults and other defects of computer systems

LO3. Replace and provide remedies for defective computer parts

LO4. Test run system and networks

ASSESMENT CRITERIA

Refer to assessment criteria o learning outcomes # of this module.

- Plans and proceedings conform to the job requirements are formulated.

- OHS policies are carried out along with the job requirements

- Coordination with the teacher concern and client is taken into consideration before any implementation is carried out.

- Required materials for the job are obtained and validated against the requirements of the task.

- Appropriate tools equipment and testing devices are requested before the proper operation and safety.

- Computer system network defects are confirmed against job requirements.

- Standard procedures for fault and problems-diagnosing are done according to requirements.

- Emergency procedures are put under control accordance with the established procedures.

- Accidental events or conditions are responded according to the established standard operating procedures.

- Appropriate personal protective equipment is used.

- Necessary corrections and improvements or adjustments are executed with the approval of the client and the teacher in charge.

- Discarding or replacement of defective components /parts abiding with environmental laws and regulations is carried out.

- Accidental events or conditions are responded to according to the established standards and procedures.

- OHS standards are considered in the choice of equipment.

- Test run the computer system is executed for ensuring safe operation.

- Accidental events or conditions are responded to according to established standards and procedures.

- An accomplishment report is submitted to teachers concerned in compliance with the subject requirements.

TECHNICAL TERMS

Fuse – Protective device against power surges

Firmware- is a combination of hardware and software, it is a program integrated on a chip.

Defrag- process of reorganizing and rewriting files.

Form factor - a standard size and shape of computer subsystem

People ware -	the persons using the computer in the goal of finding solutions to a better and improved daily life. These can range from the basic word-processing to the more advanced system programming.

#### Hardware - the physical and tangible component of electronic data processing. These are the monitors, keyboard, mouse, all input/output devices, as well as internal memory system.

###### Software - the intangible element composed of programs that instruct computers what to do.

Electricity - a form of energy comprising certain charge particles, such as electrons and protons.

Power 	- is the rate in which electric energy is fed or taken from a device measured in watts.

Voltage - is the term used to designate electric pressure that exists   between two points.

PPE - Personal Protective Equipment

BOOT - is the process of turning on the computer unit.

#### CMOS - Complementary Metal Oxide Semi-conductor

BIOS - Basic Input/Output System

###### DOS - Disk Operating System

ROM - Read Only Memory

POST - Power On Self Test

DSL – Digital Subscriber Line

UTP cable – Unshielded Twisted Pair cable

UPS – Uninterruptible Power Supply

VGA – Video Graphic Adapter

USB – Universal Serial Bus

CPU – Central Processing Unit

OHS – Occupational Health and Safety

LCD – Liquid Crystal Display

CRT – Cathode Ray Tube

RAM – Random Access Memory

DIMM – Double In-line Memory Module

I/O – Input/Output

Program course		: Computer Hardware Servicing NCII

Unit of Competency	: Diagnose and Troubleshoot Computer

System

Module	: Diagnosing and Troubleshooting of Computer

System

LO.1 Title	: Formulate Plans and Prepare for Diagnostic

Procedure for Computer Troubleshooting

Assessment Criteria:

- Plans and proceedings that conform to the job requirements are formulated.

- OHS policies are carried out along with the job requirements

- Coordination with the teacher concerned and client is taken into consideration before any implementation is carried out.

- Required materials for the job are obtained and validated against the requirements of the task.

- Appropriate tools equipment and testing devices are requested before the proper operation and safety.

- Computer system network defects are confirmed against job requirements.

Resources:

| Equipment/Facilities | Tools & Instruments | Supplies & Materials |
| --- | --- | --- |
| Server Computer peripherals Desktop computers Glasses Mask Gloves Anti-static wrist strap USB Flash drive | Multi-tester Diagnostic software Appropriate software Assorted pliers Assorted screw drivers Soldering gun Allen key | Connectors, RJ45 Adaptors Bus wires and cables Appropriate software Computer storage media |

References:

1. McLaughlin, Robert, Sasser,Susan, Ralston,Mary.Fix Your Own PC.Philippine Graphic Arts, Inc Tandang Sora St.Caloocan City

2. Meralco Faoundation. Microcomputer Servicing Plus. Pasig City, Philippines.

3. Legaspi, Carlos, Caiña, Mark Anthony. Operate A Personal Computer. Dasmariñas Computer Learning Center.Dasmariñas,Cavite, Philippines

4. Bigelow, Stephen J. PC Technician’s Troubleshooting ,McGaw Hill

5. www.helpwithpcs.com

6. http://en.wikipedia.org

- www.techsoup.org

8. www.howstuffworks.com

9. www.microsoft.com/technet/network

INFORMATION SHEET 1.1

Plan and Preparing Diagnostic Procedure

PC Diagnosing

Probably the most frustrating problem computer users run into are startup problems, where your computer won’t boot. Equally annoying are error messages you constantly run into during your computer’s startup process. In this module you will be given a few tips on how you can avoid some of the most common problems that happen right after your computer turns on.

Troubleshooting Plan for Personal Computers

How to Troubleshoot the Computer?

Here you will learn the basic troubleshooting methods of your computer.

- Trial and error: When you find a faulty component in your computer,  check it with the other computers so that you can make sure whether the fault is in the component or not.

- Check cables: In case of any device failure, check all the cables of your computer such as data cables, power cable, internal circuitry cables  and make sure that all these are plugged in and working fine.

- Hardware settings: Check the hardware settings in the CMOS and in the device manager of the system and make all the device drivers are up to date and all the cards are plugged in properly.

- Notice changes: When you notice a software or hardware error in your computer, determine what was changed before the problem occurred

- Event viewer: In the event viewer, you will find the error or warning messages associated with any faulty hardware or software.

- Make notes: Troubleshooting is a big learning option and we can learn a lot when we face any kind of troubleshooting in our computer. Make notes including the error messages and their solutions, so that you have a record on how a certain problem occurred and how did you solve it.

Sample Diagnostic Plan

List down all possible components to be checked based on the symptoms.

| Symptoms: Dead Computer Monitor | Good | Defective | Remedy |
| --- | --- | --- | --- |
| AC outlet |  |  |  |
| AVR |  |  |  |
| AVR fuse |  |  |  |
| Monitor Power Cable |  |  |  |
| Monitor Switch |  |  |  |
| Power Supply |  |  |  |

Common Trouble for Computer Units

- Double check the power connections.

- Voltage Regulator and power supply could cause power failure in the computer unit.

- Check the power cords and cable connectors in your computer unit.

- Unseated card. Loose cards could cause it to malfunction.

- Do you have ink or toners in your printer? Check the ink toners/cartridges in your printers.

- Check the boot sequence configuration in the advance BIOS (Basic Input/Output Unit) setup.

Diagnosing Network Connection

These are the things to look for if a PC will not connect to the internet or network.

- First check the cable connecting to the network card into the network hub.

- Check the back of the computer to see if the network card light is on

- Check the network cable

- Check the network HUB

OPERATION SHEET 1.1

Diagnostic Plan

Equipment, Tool, Materials:

Equipment

Computer unit

Tools

Multi-tester

Philip Screw driver

Materials

Bond paper

Ruler

Pencil/Eraser

Diagnose a Computer Power Supply

Create a diagnostic plan for troubleshooting a power supply with the use of the following tools, materials and equipment.

You will be assessed using the following criteria

| Evaluation: CRITERIA | Rating |
| --- | --- |
| 1. Sequence of steps in diagnosing is followed. | 20% |
| 2. Observance of safety precautions. | 20% |
| 3. Appropriate tools are used in diagnosing. | 30% |
| 4. Creating a diagnostic plan for troubleshooting. | 30% |
|  | 100% |

### INFORMATION SHEET 1.2

Tools for Testing Computer System

Tools and equipment play a vital role in troubleshooting; it helps the user to determine the errors found in your computer hardware and network.

Tools used to test hardware problems:

1. Screw drivers-is used to install and remove screws in your computer unit.

2. Pliers and tweezers- is used for picking small parts in your computer unit.

3. Soldering iron- is primarily used for connecting terminals in your power supply and circuit board with the use of a soldering lead.

4. Anti-static wrist strap, mat and spray- are used to eliminate electrostatic discharge in your work area.

5. Lens cleaner-is used for cleaning optical media, such as DVD-ROMS and CD-writers.

6. Thermal paste-is a paste used for heat dissipation for your processor.

Network Troubleshooting Tools

1. LAN Tester – is a device used to test the network connection..

2. Crimping tool- is a device used to crimp the RJ45 connector to the UTP cable.

Self Check 1.1

Place your answers on your notebook:

1. Enumerate the six tools used for troubleshooting.

a.

b.

c.

d.

e.

f.

2. Enumerate the two network troubleshooting tools.

a.

b.

Program course		: Computer Hardware Servicing NCII

Unit of Competency	: Diagnose and Troubleshoot Computer

System

Module	: Diagnosing and Troubleshoot of Computer

System

LO#2 	: Diagnose Computer and Other Defects

Faults of Computer Systems

Assessment Criteria:

- Standard procedures for fault and problems-diagnosing are done according to requirements.

- Emergency procedures are put under control accordance with the established procedures.

- Accidental events or conditions are responded according to the established standard operating procedures.

- Appropriate personal protective equipment is used.

Resources:

| Equipment/Facilities | Tools & Instruments | Supplies & Materials |
| --- | --- | --- |
| Server Computer peripherals Desktop computers Glasses Mask Gloves Anti-static wrist strap USB Flash drive | Multi-tester Diagnostic software Appropriate software Assorted pliers Assorted screw drivers Soldering gun Allen key | Connectors, RJ45 Adaptors Bus wires and cables Appropriate software Computer storage media |

References:

- McLaughlin,Robert, Sasser,Susan, Ralston,Mary.Fix Your Own PC.Philippine Graphic Arts, Inc Tandang Sora St.Caloocan City

- Meralco Faoundation. Microcomputer Servicing Plus. Pasig City, Philippines.

- Legaspi,Carlos, Caiña, Mark Anthony. Operate A Personal Computer. Dasmariñas Computer Learning Center.Dasmariñas,Cavite, Philippines

- Bigelow,Stephen J. PC Technician’s Troubleshooting ,McGaw Hill

- www.helpwithpcs.com

- http://en.wikipedia.org

- www.techsoup.org

- www.howstuffworks.com

- www.microsoft.com/technet/network

INFORMATION SHEET 2.1

Personal Protective Equipment

Personal Protective Equipment includes:

- Safety Precautions

- Preventive Maintenance

- Protective Devices

- Accident Reports

Safety precautions

Proper preparation is the key to a successful built. Before you begin, make sure that you have the tool you will need, and secure a clear well-lit workplace. Gather all the components you’ll be using and unpack them at the same time. Find a dry, well-ventilated place to do your work, you should choose an area without carpets, because it tends to create static electricity. Always keep in mind that personal protection is one of the traits of a good technician.

Preventive Maintenance

Maintenance is keeping something in working order. It includes repair, testing, adjusting, and replacing parts of a computer or a peripheral.

Types of Preventive Maintenance

- Active

- Passive

Active – this is carried out before problems develop in a computer unit.

Passive – this is carried after problems have developed in the computer unit.

Personal Protective Devices

- Anti-Static Devices

- Power Surge Protector Devices

Anti-Static devices

These are the devices used to protect computer units from electro static discharge.

- Anti-static Wrist Strap

- Anti-static Mat

- Anti-static Bag

Power Surge Protector Devices

An appliance designed to protect electrical devices from voltage spikes. A surge protector attempts to regulate the voltage supplied to an electric device by either blocking or by shorting to ground voltages above a safe threshold.

- Automatic Voltage Regulators (AVR)

- Uninterruptible Power Supply  (UPS)

Accident reports

Forms used to give specific details with regards to the accidents happed in the laboratory during experiments.

Accident reports contain the following details:

- Name of the person injured

- Date and time of the accident

- Type of injury

- First aid given

- Action taken to prevent further accidents

Accident report sample form

| Form No: | Accident Report Form | Date: |
| --- | --- | --- |
|  |  | Rm. No: |
| Name: | Yr/Sec: |
| Type of Injury | Cause of Injury | Remedy |

### INFORMATION SHEET 2.2

Techniques for Diagnosing Computer System

Techniques for diagnosing computer system

- Computer Diagnosis

- Rules In Diagnosing Computer System

- Factors Causing Computer Failures and Defects

- Problem Isolation

- Component Isolation

Computer Diagnosis

Sometimes when the problem with a system is not totally apparent and the problem may be intermittent, using a basic common diagnostic procedure may help determine what is wrong. This procedure has a number of steps that, if followed each time, can be of help.

## Rules in Diagnosing Computer System

- Know the facts

- Educate oneself on all aspects and operation of computer parts.

- Continuous learning on computer technology.

- Use your common sense

- Focus on Field Replaceable Units

- Identify the different types of FRU that can be used for replacement or subassembly.

- Proper assembly and disassembly

Factors Causing Computer Failures and Defects

- Peopleware

- Firmware

- Software

- Hardware

- Static(ESD)

- Electricity

Peopleware

- Untrained personnel would probably damage programs in PC.

Firmware

- Programs or software burnt in chips may be corrupted.

##### Software

- Corrupted operating systems would cause the system to fail.

##### Hardware

- Defective hardware components would lead to computer malfunction.

- Hardware conflicts and viruses can hinder your computers performance.

ESD (Electro Static Discharge)

- Electro static discharge can easily damage sensitive components in your computer.

###### Electricity

- Incoming supply from AC outlet must be regulated, power surges can damage computer units.

Problem Isolation

Problem isolation is a detective work in which you need to determine what is out of the ordinary by making detailed observation of what is not working normally and record any information as you proceed. The information you will be able to gather will help diagnose your computer. You need to observe wisely. Look for any abnormalities in the unit, any change in smell or foreign smell, listen to all the sounds, and error codes.

Component Isolation

This section will aid in determining components in your system which are failing. First, most systems have 3 major components; monitor, system unit, and printers. Some have multiple external devices. To troubleshoot, you need to isolate major components which are failing to operate.

### Figure 1. Computer system connections

###### OPERATION SHEET 2.1

Faulty Connection of Computer Peripherals

Equipment, Tools, and Materials:

System unit,

Monitor,

Keyboard

Mouse

Printer

Power plugs

AVR

.

Common Connection Errors

Given with the different equipments, diagnose and identify common connection errors messages and symptoms in computer system.

You will be assessed using the following criteria

| Evaluation: CRITERIA | Rating |
| --- | --- |
| 1. Sequence of steps in diagnosing is followed. | 40% |
| 2. Observance of safety precautions. | 20% |
| 3. Standard procedures in diagnosing are performed. | 40% |
|  | 100% |

Program course		: Computer Hardware Servicing NCII

Unit of Competency	: Diagnose and Troubleshoot Computer System

Module	: Diagnosing and Troubleshoot of Computer System

LO.3 Title                  : Replace and provide remedies for defective computer parts

Assessment Criteria:

- Necessary corrections and improvements or adjustments are executed with the approval of the client and the teacher in-charge.

- Discarding or replacement of defective components/pats abiding with environmental laws and regulations is carried out.

- Accidental events or conditions are responded to according to the established standards and procedures.

- OHS standards are considered in the choice of the equipment.

Resources:

| Equipment/Facilities | Tools & Instruments | Supplies & Materials |
| --- | --- | --- |
| Server Computer peripherals Desktop computers Glasses Mask Gloves Anti-static wrist strap USB Flash drive | Multi-tester Diagnostic software Appropriate software Assorted pliers Assorted screw drivers Soldering gun Allen key | Connectors, RJ45 Adaptors Bus wires and cables Appropriate software Computer storage media |

Reference:

- McLaughlin,Robert, Sasser,Susan, Ralston,Mary.Fix Your Own PC.Philippine Graphic Arts, Inc Tandang Sora St.Caloocan City

- Meralco Faoundation. Microcomputer Servicing Plus. Pasig City, Philippines.

- Legaspi,Carlos, Caiña, Mark Anthony. Operate A Personal Computer. Dasmariñas Computer Learning Center.Dasmariñas,Cavite, Philippines

- Bigelow,Stephen J. PC Technician’s Troubleshooting ,McGaw Hill

- www.helpwithpcs.com

- http://en.wikipedia.org

- www.techsoup.org

- www.howstuffworks.com

- www.microsoft.com/technet/network

INFORMATION SHEET 3.1

Proper Replacement of Components or Parts

Computer Parts Replacement

Replacing computer parts and peripherals you need to consider the following factors:

- Compatibility of the component or part

- Consider the component specification

- Components form factor

Compatibility of the Component

When replacing computer parts you should check if it is compatible with your unit. Double check on your computer manual if the component you are replacing is compatible or not with the unit because this may lead to system crash.

Component Specification

This focuses on the specification of the component. Check if the voltage rating, current rating, memory size and frequency matches your computer unit.

Form factor

The components’ manufacturer should be considered. Check if the unit you are trying to repair or upgrade is generic or branded units. Branded units have their own set of components compatible only to their units, while genetic types can be used only to generic type of units.

List of Components Commonly Replaced in a Computer System

Memory- is technically any form of electronic storage; it is used most often to identify fast, temporary forms of storage. It is commonly called RAM (Random Access Memory).

Video Cards- is also referred to as a graphics accelerator, is an item of personal computer hardware whose function is to generate and output images to a display.

Network Interface Card – is also known as LAN card. A PC interface to network cabling. It is a piece of computer hardware designed to allow computers to communicate over a computer network

Hard disk drive – is a fixed computer storage medium

Motherboard – is also known as the mainboard. It contains circuits that perform various functions.

Processor – is also known as CPU or the Central Processing unit

General Safety Tips and Reminders

- Observe good housekeeping in the area of the machines during and after maintenance.

- Place removed covers and other parts in a safe place, away from all personnel, while you are servicing the machine.

Dress for the Job

- Keep your tool case away from walk areas so that other people will not trip over it.

- Do not wear loose clothing that can be trapped in the moving parts of a machine. Ensure that your sleeves are fastened or rolled up above your elbows. If your hair is long, use hair net or hair cap.

- Insert the ends of your necktie or scarf inside clothing or fasten it with a nonconductive clip, approximately 3 inches from the end.

- Do not wear jewelry, chains, metal-frame eyeglasses, or metal fasteners for your clothing.

- After service, reinstall all safety shields, guards, labels, and ground wires. Replace any safety device that is worn out or defective.

- Finally, reinstall all covers correctly before returning the unit to the customers.

Electrical safety

Electric current from power, telephone, and communication cables can be hazardous. To avoid personal injury or equipment damage, disconnect the attached power cords, telecommunications systems, networks and modems before you open the server/workstation covers, unless instructed otherwise in the installation and configuration procedure.

Precautions

- Disconnect all power before:

  - Performing a mechanical inspection

  - Working near power supplies

  - Removing or installing main units

- Before starting work on the machine, unplug the power cord.

- Never assume that power has been disconnected from a circuit. First, check that it has been powered-off.

- Always look carefully for possible hazards in your work

  - Moist floors

  - Non-grounded power extension cables

  - Power surges.

- If an electrical accident occurs:

  - Use caution

  - Switch off power

  - Send another person to get medical aid

Safety Inspection Guide

- These steps will help you to identify potentially unsafe conditions on these products:

  - Check exterior covers for damage (loose, broken, or sharp edges)

  - Power-off computer. Disconnect the power cord.

  - The power cord should be the appropriate type.

  - Insulation on the power cord must not be frayed or worn out.

  - Remove the cover.

  - Check for any obvious alteration. Use good judgment as to the safety of any alterations.

  - Check for worn out, frayed or pinched cables.

  - Check that the power-supply cover fasteners (screws or rivets) have not been removed or tampered with.

Self Check 3.1

Place your answer on your notebook

1 .Give the functions of each component.

- Memory

- Video card

- NIC

- Motherboard

- HDD

2. Factors to consider when replacing a component.

1.

2.

3.

INFORMATION SHEET 3.2

Adjustments, Modifications and Upgrading

# Upgrading Your Computer Components

To upgrade means to change some parts with faster and better performing ones. These parts may even cost less and more powerful.

Commonly Upgraded Computer Parts:

Monitors- replaced old CRT monitors to new LCD monitors.

Optical drives- old cd-rom drives are commonly replaced with DVD-ROM and DVD writers.

Hard Drives- small capacity hard drives are replaced with faster and high capacity hard drives.

Keyboards and mouse- keyboards and mouse are commonly replaced with optical mouse and wireless keyboards.

RAM (Random Access Memory)- upgrading the computer’s memory  or RAM    speeds up the performance of the computer

Video cards- upgrade computer’s graphics card to improve the computers performance in terms of graphics and games.

Processors- replacing the possessors increases the data processing speed.

Modem- installing a modem enables your computer to connect to the internet.

How to Speed up the Computer

1. Defragmenter utility: Automatically analyzes the empty disk space on the hard disk and defrag all scattered files.

2. Shutdown Unnecessary programs: Close all unwanted programs at the Windows startup and this will automatically increase the windows loading time and speed of the computer will also be increased.

3.Increased memory: increasing the memory in the system will result to exceptional speed of your computer.

4. Disk Cleanup: You can delete unwanted programs and files from your computer and this will be helpful in increasing the speed.

5. Empty Recycle Bin: Delete all the files and folders from the recycle bin and you will get the space of C drive for reusability.

Memory Upgrade

To make your computer faster you can upgrade its memory, here are the steps in upgrading your computers memory

1. Remove the memory modules from the slot.

| 2. In Fig 1.2 the notches we have marked as A are used for the ejector clip on the DIMM slot. The notches we have marked as B are used to align the memory module with the DIMM slot key C as shown in Fig 1.3. In Fig 1.3 you can see the ejector clips (D), using your finger, push these into the down position as shown in Fig 1.3 this allows the memory to be inserted. |  |
| --- | --- |

| 3. Now you are ready to install the module, ensuring the notches line up with the keys gently but firmly push the memory into the slot until it is seated fully(see Fig 1.4), the ejector clips should rise to the vertical position as shown in Fig 1.5. 4. Now your memory is installed. Be sure you haven't loosened any cables while working and also ensure that the memory module is fully seated and the ejector clips are in the vertical position. |  |
| --- | --- |

Video card Upgrade

Installing the video card 

Next take the video card (hold it by the edges) and line it up with the slot paying careful attention to the alignment notch, when it is aligned correctly press gently but firmly until the card is seated fully and evenly into the slot (see fig 1.3).

When you are happy that the card is firmly in place, insert the fixing screw   fig 1.4 and check to make sure you haven't loosened anything during installation. 

Replace the case cover and reconnect the mains power.

When you reboot your machine Windows (or other OS) should find the card automatically, it may then ask you to insert the disk/CD that came with your video card, insert the CD and follow the on-screen instructions to install the video card driver.

Hard Drive Upgrade
The first thing to do (after removing the case covers) is to locate the drive bay where the hard drive will go (see fig 1.3 below). 

In our example in fig 1.3 above we have a drive already in the bay so you can see more clearly where it should be situated.

The next step is to attach the IDE and power cables. 

In fig 1.4 below you can see a standard IDE Cable, note there are 3 connections (notice the difference in distance between the connectors), connection A plugs into the motherboard and then the slave and master connections are used for IDE devices such as hard drives, if you are only installing one drive or the new drive is to be the master then use the master connector, if the drive is to be the slave then use the slave connector. 

The IDE cable will be marked down one side with a red or black strip, this denotes Pin 1, match this with the Pin 1 indicator on the back of the hard drive. 

The power cable you will find in your case attached to your power supply, you can see an example below in fig 1.5

OPERATION SHEET 3.1

Hardware Upgrade

Tool, Materials, and Equipment

Tools

Philip Screw Deriver

Anti-static wrist strap

Anti-static mat

Equipment

Network Card

Network Card Upgrade

Given the tools and materials, upgrade your computer by installing a network card.

You will be assessed using the following criteria

| Evaluation: CRITERIA | Rating |
| --- | --- |
| 1. Observance of safety precautions | 30% |
| 2. Appropriate tools are used in upgrading | 30% |
| 3. Necessary improvement and adjustment are done in terms up upgrading. | 40% |
| . | 100% |

Program course		: Computer Hardware Servicing NCII

Unit of Competency	: Diagnose and Troubleshoot Computer System

Module	: Diagnosing and Troubleshooting of Computer

System

LO.4 Title                  : Test-run the computer system

Assessment Criteria:

- Test-run of the computer system is executed for ensuring safe operation.

- Accidental events or conditions are responded to establishe standards and procedures.

- An accomplishment report is submitted to teachers concerned in compliance with the subject requirements.

Resources:

| Equipment/Facilities | Tools & Instruments | Supplies & Materials |
| --- | --- | --- |
| Server Computer peripherals Desktop computers Glasses Mask Gloves Anti-static wrist strap USB Flash drive | Multi-tester Diagnostic software Appropriate software Assorted pliers Assorted screw drivers Soldering gun | Connectors, RJ45 Adaptors Bus wires and cables Appropriate software Computer storage media Cable tie |

Reference:

- McLaughlin,Robert, Sasser,Susan, Ralston,Mary.Fix Your Own PC.Philippine Graphic Arts, Inc Tandang Sora St.Caloocan City

- Meralco Faoundation. Microcomputer Servicing Plus. Pasig City, Philippines.

- Legaspi,Carlos, Caiña, Mark Anthony. Operate A Personal Computer. Dasmariñas Computer Learning Center.Dasmariñas,Cavite, Philippines

- Bigelow,Stephen J. PC Technician’s Troubleshooting ,McGaw Hill

- www.helpwithpcs.com

- http://en.wikipedia.org

- www.techsoup.org

- www.howstuffworks.com

- www.microsoft.com/technet/network

INFORMATION SHEET 4.1

Testing Computer System

Three Major Components of Computer System:

- Hardware

- Software

- Firmware

Test Your Hardware

Checking your computer hardware and its peripherals

1. Computer Monitor and its peripherals

- Monitor and interface cables

- Video card

- Monitor power cable

2. Keyboard and Mouse

- Keyboard connector

- Mouse Connector

3. I/O port and devices

- Connection between the I/O port and the peripheral device

- A faulty cable between the I/O port and the peripheral device

- A faulty peripheral device

- Incorrect settings in the System Setup program

- Incorrect settings in the system's configuration files

- Faulty I/O port logic on the system board

4.  Power supply

- Power cord

- Fuse

Testing Your Software

Check the different software installed in the computer.

1. Operating system

- Run live updates for your operating systems to get the latest patches and protection for your OS.

- Run registry scanners to check the OS registry configuration

2. Application Software

- Check for live updates

3. Anti-virus software

  - Run anti-virus program

  - Check for virus signature updates

  - Check for spyware updates

Test Your Firmware

Firmware- a combination of hardware and software integrated on a chip.

How do you test your firmware?

Example:  Check for the correct configuration on your firmware, you can accomplish this by configuring the BIOS in the computer

Sample Accomplishment Report Form

| Task to be accomplished | Status |
| --- | --- |
| Hardware component testing | Working properly | Not working properly |
| Software testing | Status |
|  | Working properly | Not working properly |

OPERATION SHEET 4.1

Testing a Computer Unit

Equipment, Tools, and Materials:

Tools

Multi-tester

Screw driver

Equipment

Computer unit

Monitor

Keyboard and mouse

Power cables

Materials

Bond paper

Ruler and Pencil

Hardware Testing and Documentation

Test the following computer peripherals and equipment with the use of the tools provider. Document your testing with the use of an accomplishment form.

| Assigned Task | Condition |
| --- | --- |
| Hardware component testing | Working properly | Not working properly |
| Computer monitor |  |  |
| Power supply |  |  |
| Keyboard |  |  |
| Mouse |  |  |

You will be assessed using the following criteria

| Evaluation: CRITERIA | Rating |
| --- | --- |
| 1. Sequence of steps in testing is followed. | 20% |
| 2. Observance of safety precautions. | 20% |
| 3. Appropriate tools are used in testing. | 30% |
| 4. Creating a accomplishment report. | 30% |
|  | 100% |

INFORMATION SHEET 4.2

Enumerating unpredicted events

Error Beep codes

When a PC is first switched on or reset it performs a special diagnostic test called a POST (Power-On Self Test), to check all of the components in the PC the POST program sends out a signal to each device initializing each device's built-in self test procedure.

The POST test is a two stage process:

1. First it will check all of the basic components including among other things the system clock, the processor, RAM, the keyboard controller and the Video

2. After the video has been tested the BIOS will then indicate any errors encountered by displaying either a numeric code or a text message on the screen.

When a device fails the first part of the POST, the BIOS will send a series of beeps from the PC's speaker (internal) to inform the PC user that there is a problem, these beeps are coded allowing the user to diagnose the troublesome component. 
 When the POST has been completed successfully the PC will make a short beep to let the user know everything is as it should be.

Three major brands of BIOS chip

- AWARD BIOS

- Phoenix BIOS

- AMI BIOS

Each type of BIOS chip has it own error code

AMI BIOS ERROR BEEP CODES

| Indicator | Error message | Solutions |
| --- | --- | --- |
| 1 Beep 2 Beeps 3 Beeps 4Beeps 5Beeps 6 Beeps 7 Beeps 8 Beeps 9 Beeps 10 Beeps 11 Beeps | Memory refresh failure Memory parity error Memory read/write error Motherboard timer not functioning Processor error Gate A20/keyboard controller failure Processor exception interrupt Display memory read/write failure ROM checksum error CMOS shutdown read/write error Bad cache memory | Check memory Check memory Check memory Replace motherboard Replace processor Replace motherboard Replace processor Replace video card Replace BIOS chip/Motherboard Replace BIOS chip/Motherboard Replace cache memory |

Phoenix BIOS ERROR BEEP CODES

Phoenix BIOS beep codes are a series of beeps separated by a pause, for example: 
beep --- beep beep --- beep --- beep beep would be 1-2-1-2

| Indicator | Error message | Solutions |
| --- | --- | --- |
| 1-1-4-1 1-2-2-3 1-3-1-1 1-3-1-3 1-3-4-1 1-3-4-3 1-4-1-1 2-1-2-3 2-2-3-1 | Cache error BIOS ROM Checksum DRAM test rate Keyboard controller test RAM failure RAM failure data bits of low memory bus RAM failure data bits of high memory bus ROM copyright notice Test for unexpected interrupt | Check cache memory Check BIOS ROM Check DRAM Check keyboard controller Check memory Check memory Check memory Check ROM |

AWARD BIOS ERROR BEEP CODES

| Indicator | Error message | Solutions |
| --- | --- | --- |
| One long beep and two short beeps Two short beeps | Video error Non-fatal error | Replace video card Reset RAM, Check other components. |

OPERATION SHEET 4.2

Error codes

Equipment, Tools, and Materials:

Tools

Screw drivers

Anti-static wrist strap

Equipment

Computer unit

Memory Error Codes

Given the tools and equipment, identify the memory error code by removing the module in the computer unit

You will be assessed using the following criteria

| Evaluation: CRITERIA | Rating |
| --- | --- |
| 1. Observance of safety precautions. | 30% |
| 2. Appropriate tools are used in testing. | 30% |
| 3. Identifying the error code. | 40% |
|  | 100% |

Self Check 4.1

Place your answers on your notebook:

Answer the following questions

- What does the acronym POST stand for?

- Three types of BIOS chip? Enumerate the three common brands of Bios

Chip?

- Identify the following error codes:

  - 1-2-2-3

  - 1-3-4-1

  - 2-1-2-3

  - 1-1-4-1

  - 1-3-1-1

###### Answer Key 1.1

1. Tools for trouble shooting.

- Screw drivers

- Pliers and tweezers

- Soldering iron

- Anti-static wrist strap

- Lens cleaner

- Thermal paste

2. Tools for network troubleshooting:

- LAN tester

- Crimping tool

Answer key 3.1

1. Enumerate the commonly upgraded computer parts

  - Monitor

  - Optical drives

  - Hard drive

  - Keyboard and Mouse

- Enumerate the 6 steps to speed up your computer.

  - Defragmenter utility

  - Shutdown Unnecessary programs

  - Increase Memory

  - Disk Cleanup

  - Empty Recycle Bin

Answer key 4.1

1. POST- Power On Self Test

2. BIOS brands

  - AMI

  - AWARD

  - Phoenix

3.  Identify the error code:

- 1-2-2-3= BIOS ROM checksum

  - 1-3-4-1=RAM Failure

  - 2-1-2-3=ROM copyright notice

  - 1-1-4-1=Cache error

  - 1-3-1-1=DRAM fresh rate

# Text boxes

Network card

Network cable

Network HUB

Remember: Metal objects are good conductors

Close the unnecessary programs

Interface cables

Video cards

Monitor power cable

Keyboard connecter

Mouse connector

I/O circuit board

Serial ports

Parallell ports

Power cord

Power plug

Fuse

Power supply